## Slide 1: Tolerance Values beyond Wisconsin
Additional geographic areas added
  Use same formula as HBI
  Expanded scale to 0 – 10
  Sometimes had very different tolerance values
  Original HBI was scored for tolerance to organic pollution
  Most indicate tolerance to “general perturbations”, although some are still specific to particular stressors

## Slide 2: Tolerance Values
National Databases Available:
  NAWQA - Carlisle et al. 2007
    Ionic Concentrations (ammonium, sulfates, chlorides)
    Nutrients (nitrates, nitrites, phosphates)
    Dissolved Oxygen / Temperature
    Suspended Sediments
    Fine Sediments
Regional Databases Available:
  Wisconsin (Upper Midwest) – Hilsenhoff 1977, 1982
  Kansas – Huggins & Moffett 1988
    Nutrients and oxygen demanding substances
    Agricultural pesticides
    Heavy metals
    Persistent organic substances
    Salinity
    Suspended sediment
  Montana – Bukantis 1988
    Metals
  North Carolina (Southeast) – Lenat 1993
  Ohio (Midwest) – Ohio DNR 1996
  Idaho (Pacific Northwest) – Grafe et al. 2000
  Arizona – Arizona DEQ unpublished
  New England Wetlands – Hicks & Nedeau 2000
  Mid-Atlantic Highlands (VA, PA, MD) – Klemm et al. 2002
  New York – Bode et al. 2002
  California (Southwest) – Richards & Rogers 2006
  Georgia – Georgia DNR 2007

## Slide 3: Species Traits
Define the “ecological niche” for each taxon
  Theoretically, every species has its own niche in which it
  thrives. We use broad traits to describe those niches.
Easier to understand than Latin scientific names!
Traits available in the Benthic Invert Taxa List
  Functional Feeding Groups
  Behavior/Habits
  Voltinism
  Temperature
  Morphology
  Habitats
    Benthic
    Estuarine / Marine
    Springs
    Temporary habitats
  Ecology
    Lotic waterbodies
    Lentic waterbodies
    Current
    Substrate size
    Emergence period

## Slide 4: Functional Feeding Groups
Filter-Collectors (FC)
Gather-Collectors (GC)
Omnivores (OM)
Parasites (PA)
Plant Piercers (PI)
Predators (PR)
Scrapers (SC)
Shredders (SH)

## Slide 5: Behavior/Habits
Burrowers (bu)
Climbers (cb)
Clingers (cn)
Skaters (sk)
Sprawlers (sp)
Swimmers (sw)

## Slide 6: Voltinism
Multivoltine
(> 1 generation/yr)
Univoltine
(1 generation/yr)
Merovoltine
(>1 yr/generation)

## Slide 7: Temperature
Stenothermal
Hypercold
Stenothermal
Cold
Eurythermal
Cool
Eurythermal
Warm
Eurythermal
Hot
Trait is based on the range of temperatures in which a particular taxon may be found
Stenothermal – restricted to a relatively narrow temperature range
Eurythermal – can tolerate a relatively wide range of temperatures
Temperature

## Slide 8: Sunbeam Hot Springs, ID
Chart: Sampling Date
| Oct '00 | Apr '01 | Aug '01 | Oct '01 | Apr'02
 | 97 | 117 | 86 | 167 | 163
Hydroscapha natans

## Slide 9: Temperature
Grafe et al. 2000
- Idaho
- Based on measurements
during sampling
Vieira et al. 2005
- North America
- Based on statements
in literature (e.g., “found
in cool streams”)

## Slide 10: Temperature
Numeric data:
  Calculated preferences for 125 cold-water taxa (Grafe et al. 2000)
  Max/Min reported for genera in litt. (Vieira et al. 2005)
  Calculated preferences for 72 genera
  (Yuan 2006)

## Slide 11: Morphology
Size
  S, M, L
  Combinations (S/M, etc.)
Shape
  Bluff (blocky)
  Dorsoventrally flattened
  Round (humped)
  Streamlined / fusiform
  Tubular

## Slide 12: Habitats
Richards & Rogers (2006) - California
  Benthic
  Lotic
  Lentic
  Estuarine/Marine
Vieira et al. (2005)
  Cold springs
  Warm springs
  Temporary lotic habitats
  Temporary lentic habitats

## Slide 13: Waterbody Size Preference
Based on Vieira et al. (2005)
  Literature statements (e.g., “collected in headwaters”)
Preference assigned on scale of 1 – 5
  If reported from small waterbodies – 1
    Headwater streams
    Small ponds
  If reported from midsize waterbodies – 3
    Stream order 2 – 4
    Small lakes
  If reported from large waterbodies – 5
    Stream order 5+
    Large lakes

## Slide 14: Current Preference
Based on Vieira et al. (2005)
  Literature statements (e.g., “prefers slow currents”)
Preference assigned on scale of 0 – 3
  If reported from still water – 0
  If reported from slow water – 1
  If reported from fast water – 2
  If reported from torrential water - 3

## Slide 15: Substrate Size Preference
Based on Vieira et al. (2005)
  Literature statements (e.g., “found in gravel streams”)
Preference assigned on scale of 0 – 10
  Silt/mud (0)
  Sand (1)
  Gravel (4)
  Cobble (7)
  Boulder (10)
Also, % sand/fines tolerance (Yuan 2006)
  72 genera
Chart: Minimum grain size (Φ)
| 5.9657842846620879 | 5.0115879742752076 | 3.9885043611621729 | 3 | 2.2378638300988865 | 2 | 1.2344652536370222 | 0.73696559416620622 | 0
Upstream | 0.00231 | 0.0038124 | 0.041371 | 0.12196 | 0.15783 | 0.34984 | 0.57387 | 0.99898 | 0.99945
Middle | 0.0034641 | 0.01806 | 0.09306 | 0.22285 | 0.27574 | 0.52056 | 0.7202 | 0.99656 | 0.9981
Downstream | 0.0029872 | 0.0077275 | 0.050598 | 0.14718 | 0.18997 | 0.42047 | 0.63144 | 0.99606 | 0.9993
Monitoring | 0.0018794 | 0.0040215 | 0.047921 | 0.13839 | 0.17937 | 0.41273 | 0.61786 | 0.99644 | 0.99822

## Slide 16: Emergence
From Vieira et al. (2005)
  Literature statements (e.g., “emerges in July”)
  Assigned by season
    Winter (1)
    Spring (2)
    Summer (3)
    Fall (4)

## Slide 17: Colorado Multimetric Index (MMI)
Used by CDPHE to establish whether stream segments are attaining aquatic life use or impaired
Other states have developed their own (or are developing one)

## Slide 18: Bioregions
State divided into 3 “bioregions”
  Mountains
  Plains
  Transitional
    Everything that isn’t “clearly” mountains or plains
    Calculated based on Ecoregion, elevation, & slope

## Slide 19: What is included?
 | Mountains | Plains | Transitional
Number of Taxa | X |  | 
Insects |  | X | 
Non-insect taxa |  | X | X
Ephemeroptera | X |  | 
Ephemeroptera + Plecoptera |  |  | X
Chironomidae |  |  | X
Beck Biotic Index | X |  | 
Dominant Taxa |  | X | 
Sensitive Plains Families |  | X | X
Predators + Shredders | X | X | X
Clingers | X |  | X
Sprawlers |  | X | 

## Slide 20: Calculations
The value for each metric is converted to a score
  Formula is based on the 95th percentile of reference site scores
Scores are averaged for Final MMI Score
MMI Score is compared to thresholds that indicate attainment or impairment

## Slide 21: Questions, Comments?